## Slide 1: Augmenting Amdahl’s Second Law: A Theoretical Model for Cost-Effective Balanced HPC Infrastructure for Data Driven Science
Arghya Kusum Das, Jaeki Hong, Sayan Goswami, Richard Platania, Wooseok Chang, Kisung Lee, SeungJong Park

## Slide 2: Overview
Big data HPC demands more compute cycles and more I/O bandwidth
System designers need to reduce cost with expected performance
Theoretical model to optimize cost/performance by quantifying the system balance between CPU, I/O and memory subsystem
  Easy to use
  Simple
  Additive model
Outcome considering Intel Xeon processor
  0.17 GBPS I/O per CPU GHz
  3GB DRAM per CPU GHs
3 Clusters are evaluated
  SuperMikeII, SwatIII and CersesII
TeraSort, WordCount and Human Genome Assembly
  CeresII resembles the optimal produced
  85% gain in Hadoop stage and 40% gain in Giraph stage of Human genome assembly

## Slide 3: Related work
Experimental Evaluation
  Experiment on real cluster hardware. E.g., our previous study
  No quantitative analysis
Simulation of big data software
  Generate virtual MR job on small data to estimate performance
  Time consuming, can not asses time for big data, lots of alternatives
Analytical performance model of big data software
  Faster than simulation as it abstract away several parameter. However, too many alternatives to consider.
  Good for selecting between two existing infrastructure but not for proposing new one

## Slide 4: Related Work
System characterization with Amdahl’s second law
  Realistic approach, most relevant to this work
  Proposed by Amdahl (1bit of IO/S IPS, 1byte of memory per IPS is required for system balance) and then revised by Gray
  Used for System characterization and to propose alternative hardware
  Bell and Gray (MS) characterized supercomputers
  Cohen (IBM) studied network interconnect
  Szalay and Bell proposed Amdahl’s balanced blade architecture to balance performance and power consumption. No change in the law is required
We balance performance and cost
Original form do not consider cost. Hence, we modified it for our purpose